## Slide 1: GazeEEGLabImporter
Date: 10/12/2013
Version: 1.0
Produced by: Anton Andreev, Gipsa-lab/CNRS
Contact: andreev.anton@gipsa-lab.grenoble-inp.fr

## Slide 2
BrainAmp and Eyetracker
- .eeg, .vhdr, .vmrk, .asc
Gtec and Eyetracker
- .hdf5, .asc
1) Data acquisition
hdf5 -> .eeg, .vhdr, .vmrk
2) Format conversion
-> asc.mat, eeg.mat
3) Synchronization between the EEG and the eye-tracker
SoftEye,
BrainVision Recorder,
G.Tec recorder
Matlab script
Matlab builder (developed by Gelu)
*.mat - > synchro_*.mat
GazeEegSynchro (developed by Gelu)
4) Import in EEGLAB
Imported in EEGLAB
GazeEegLabImporter (developed by Ronald, Anton)
In 1) the signal is acquired in a number of files. Normally these are .asc from the eyetracker and .eeg, .vmrk,.vmrk for EEG in the Brainamp format. The g.tec produces a .hdf5 file which is also converted to .eeg, .vmrk,.vmrk. After that the files are converted to .mat using the MatBuilder software. In 3) the two data streams EEG and Eyetracking data are synchronized leveraging the differences produced by the different acquisition devices (notably the “drift”). GazeEEGSynchro produces a .mat file and the total number of channels is the sum of the EEG and the eye tracker's channels. In 4) GazeEegLabImporter imports the result from 3) in EEGLAB and it is used for ERP analysis.
Offline data processing for ERP data analysis in EEGLAB

## Slide 3
Converts to EEGLAB data structures (“EEG”, ”ALLEEG”), this includes the parallel port triggers
Creates epochs – epochs are generated around a user defined list of events (usually parallel port triggers) and represent a chunk of signal. Epochs are stored in the EEG.data structure and do not represent a continuous signal
Applies filtering over each epoch – phase is preserved
Removes artifacts – EEG and non-EEG channels (deployed close to the eyes) are used to detect and attenuate the affect of eye blink artifacts. At this stage an ICA algorithm is applied developed by Gipsa-lab
Displays a figure of the average of the selected epochs per channel
4) Import in EEGLAB
Imported in EEGLAB
GazeEegLabImporter

## Slide 4
Download and unzip EEGLab 11_0_5_4b: http://sccn.ucsd.edu/eeglab/
ToolBoxGaze_gTec_EEG_v2.1.0 (if not provided)
  currently GazeEegLabImporter works on top of package ToolBoxGaze_gTec_EEG_v2.1.0
Prerequisites:
Installation:
Add to your Matlab path: ToolBoxGaze_gTec_EEG_v2.1.0
Navigate to GazeEegLabImporter folder:
  GazeEegLabImporter_Example.m (start from here)
  GazeEegLabImporter_Process.m (main execution logic)
  GazeEegLabImporter_SelectEpochs.m
  GazeEegLabImporter_BuildEpoch.m
  GazeEegLabImporter_createDataFilter.m

## Slide 5
SynchroFilename – points to a file that contains both EEG and eye-tracker data streams. These streams must be already synchronized by GazeEegSynchro
EpochEventsStr – a matlab array that specifies the parallel port event witch with combination of TimeInterval us used to generate epochs. Once GazeEeegLabImporter is executed one time you will be able to access the structure EegAcq.Events.EventTypes and see what other events are available
EpochEventsStr – a list of events that will be imported in EEEGLAB and displayed when you choose Plot->Channel data(scroll) in EEGLAB menus
TimeInterval – used to generate a time epoch around an event
StartFromTrigger – all data before this parallel port trigger is ignored
FilterData – boolean field (true/false) sets if a digital filters are applied. Default is: default is 50Hz Notch, High Pass filter 2Hz
NbNonEEGChan – this parameter is need to differentiate which channels are EEG and which are not. The non-eeg channels are expected to be last. For example if NbNonEEGChan= 5 and total number of channels is 37, then the first 37-5 channels are expected to be EEG.
Main function GazeEegLabImporter_Process parameters