## Slide 1: GazeEEGLabImporter
Date: 10/12/2013
Version 1.0
Produced by Anton Andreev, Gipsa-lab

## Slide 2
BrainAmp and Eyetracker
- .eeg, .vhdr, .vmrk, .asc
Gtec and Eyetracker
- .hdf5, .asc
1) Data acquisition
hdf5 -> .eeg, .vhdr, .vmrk
2) Format conversion
-> asc.mat, eeg.mat
3) Synchronization between the EEG and the eye-tracker stream
SoftEye,
BrainVision Recorder,
G.Tec recorder
Matlab script
Matlab builder (developed by Gelu)
*.mat - > synchro_*.mat
GazeEegSynchro (developed by Gelu)
4) Import in EEGLAB
Imported in EEGLAB
GazeEegLabImporter (developed by Ronald, Anton)
In 1) the signal is acquired in a number of files. Normally these are .asc from the eyetracker and .eeg, .vmrk,.vmrk for the Brainamp format (EEG). The g.tec produces a .hdf5 file which is also converted to .eeg, .vmrk,.vmrk. After that the files are converted to .mat using the MatBuilder software. In 3) the two datastreams EEG and Eyetracking data are synchronized leveraging the differences produced by the different acquisition devices (notably the “drift”). GazeEEGSynchro produces .mat file and the total number of channels is the sum of the EEG and the eye tracker's channels. In 4) GazeEegLabImporter imports the result in EEGLAB and it is used for ERP analysis.
Offline data processing for ERP data analysis in EEGLAB

## Slide 3
Converts to EEGLAB data structures (“EEG”,”ALLEEG”), this includes the triggers
Creates epochs
Applies filtering over each epoch – default is 50Hz Notch, High Pass filter 2Hz.
Removes artifacts – EEG and non-EEG channels (close to the eyes) are used to detect and attenuate the affect of eye blink artifacts
Displays the average of the selected epochs per channel
4) Import in EEGLAB
Imported in EEGLAB
GazeEegLabImporter